120 t telescopic crawler crane from SENNEBOGEN

With the new SENNEBOGEN 6113, the Lower-Bavarian crane manufacturer presents its biggest telescopic crawler crane yet. 120 t safe working load, a proven boom concept, and the high level of flexibility characterize the new SENNEBOGEN. With the 6113 the company, headquartered in Straubing, Germany, extends the maximum safe working load of its telescopic cranes upwards by 50%.

With more than 20 years of experience with mobile and crawler telescopic machines, SENNEBOGEN has successfully established itself on the international market. Around the world, customers from the construction industry and crane rental companies trust the reliability of the SENNEBOGEN telescopic cranes. Today with the current product range from 8 t to 80 t safe working load, SENNEBOGEN already reliably covers an broad field of work applications, for which the telescopic crawler cranes, in particular, offer many advantages for the lifting, moving, and positioning of large loads. The new SENNEBOGEN 6113 with a safe working load of 120 t is an extremely interesting solution for many crane rental companies and construction companies.

Flexible and fast in use: Full-Power Boom

The key advantage of the machine is the strong telescopic boom of the SENNEBOGEN 6113. This is - as is the case for all machines of this series - designed as Full-Power boom. Thanks to multi-cylinder technology, this maintenance-free system enables continuous telescoping and is always friction-locked. The machine can be set to any desired boom length variably and quickly via joystick. This saves time and permits effective work, particularly when boom lengths alternate in implementation. For one-cylinder systems the boom elements must be individually bolted in a complex arrangement, with the 6113, the boom can work variably and quickly at any length.

Large work range thanks to excellent mobility

Thanks to a length of 40 m, the crane covers a large work area. With fly boom and lattice boom extensions boom heights up to 70 m are achieved. However the real implementation area of the machine becomes clear when the machine moves with 100% of the load and thus promptly serves ever expansive implementation sites.

Even in rough terrain, the SENNEBOGEN 6113 is impressive with its excellent maneuverability. Tasks to max. 4 degree inclined position are possible; this can only be achieved through the particularly robust construction of the boom.

The 8 m long heavy duty traveling gear elements with up to 900 mm wide base plates, on one hand, ensure the customary low ground pressure, and on the other hand, the best possible stability, also due to the undercarriage that can be telescoped out to a track width of 5.40 m.

Minimal spatial requirements - versatile in implementation

In direct comparison with other crane concepts, the telescopic crawler crane is also convincing in terms of space requirements and versatility. Particularly relative to AT and RT cranes, the telescopic crawler crane requires over 30% less space, and thus demonstrates its advantages on narrow construction sites. Via the robust boom the machine has proven itself, not just as a crane with lifting tasks, but also in dynamic implementation, special underground engineering applications, and applications with hydraulically powered implements, such as vibrators. The implementation versatility is rounded out in combination with an elevating work platform with a load-bearing capacity of up to 1,000 kg. Thus the use range of the machine is extended with deployments in the areas of demolition and re-naturation, but also for maintenance and service tasks in each and every terrain.

Convenient to operate - easy to transport

For the driver, the maXcab comfort cab with sliding door, which can be inclined 20 degrees, offers excellent ergonomics and an excellent overview. Typical for SENNEBOGEN is the optional possibility of designing the cab with 2.70 m height-adjustability, in order to maintain the unique overview and safety advantages. An extensive safety package with LED headlights and surround cameras supports the driver in every work situation.

For crane rental companies the easy transport is a particularly important advantage. With the aid of the innovative self-assembly system of the Starlifter telescopic undercarriage, the machine can be set up in a few steps, within a short time. The SENNEBOGEN 6113 is easy to maneuver on the construction site, as well as it makes it easy to load. When the traveling gear is dismounted the transport width is reduced to 3.00 m.

Modern and clean engine technology - economical in consumption

As a telescoping crane of the new E-series, the SENNEBOGEN 6113 meets TIER 4f emission standards thanks to the powerful 168 kW Cummins engine combined with a soot particle filter and a cutting-edge exhaust aftertreatment system. In addition, the machine offers significant energy savings in Eco Mode, operating at a reduced engine speed. The new SENNEBOGEN SENCON control and diagnostics system offers a clear presentation of all operating parameters and easy, intuitive user control, as well as the ability to fine-tune machine performance and easily and quickly process error messages. In addition, the load moment limitation system can be easily and reliably monitored.

In addition, the 6113  also sets standards in the areas of maintenance and ease of service. A central lubrication point for all pivot points and the slewing ring reduces the required amount of service effort, optimizes accessibility to all service points and important components, and saves time in daily operation.

The SENNEBOGEN 6113 E-Series - in summary

# Compact and powerful: Maximum safe working loads up to 120 t, maximum boom length of 67 m

# Full-Power Boom: 4-piece telescopic boom, always friction fit, extremely robust design, variable hydraulic telescoping via joystick (no 1-cylinder step procedure), length 40 m

# Versatile and flexible in use: Robust telescoping crawler undercarriage with high stability, movement under 100% load, tasks to 4° incline and dynamic implementations are possible.

# Easy transport - fast operability: 3 m transport width, easy self-assembly system of crawler tracks, low space requirements in use

# Efficient: Powerful and efficient 168 kW Cummins diesel engine, exhaust aftertreatment in accordance with Tier 4f

# Intuitive operation: SENCON control and diagnostics system for clearly laid-out and intuitive user control

Image caption:

With the new 6113, SENNEBOGEN presents its new telescopic crawler crane with a maximum 67 m reach and impressive maximum safe working load of 120 t.