SENNEBOGEN 613 – compact 16 t telescopic crane with a new cab

SENNEBOGEN has completely redesigned its smallest telescopic crane. The popular compact crane impresses with convenient lifting capacities up to 16 t and diverse application possibilities for assembly work and construction site use. Another new feature is the Multicab 2, which is shown here for the first time as a new comfort cab.

Extremely compact dimensions as well as easy and economical transport have made the SENNEBOGEN 613 a popular helper for many construction companies and an interesting machine for the rental park. Just in time for the bauma trade fair, SENNEBOGEN presents the new generation of the mobile telescopic crane for the first time. The new machine design boasts a sturdy construction, the standard Full-Power Boom, 16 t lifting capacity and 18.8 boom length. In addition to the basic machine and the engine, the operator cab has also been completely revised.

Bauma premiere: The new Multicab operator cab 
SENNEBOGEN is showing the revised Multicab 2 operator cab for the first time at the bauma 2016; in the future, this will be installed on the small SENNEBOGEN machines as a standard feature. The new Multicab 2 combines a modern design with maximum operator comfort and ergonomic equipment. In addition to a new interior design, the cab also has a concave windshield for an optimum front view and a hinged rear window. An air conditioning system and a modern comfort seat including adjustable control elements are also standard features of the 613. This seat, which can be adjusted 1.75 m in height and allows an ideal overview of the working range, is typical of the SENNEBOGEN cranes.

Full-Power Boom for continuous telescoping

The new 613 is also equipped with the proven Full-Power Boom in addition to the existing telescopic cranes. This means that all extensions can be telescoped continuously and smoothly via joystick, allowing work in any position. Telescoping under load is also safely possible. With a maximum boom length of 18.8 m and the folding 5 m fly boom, the SENNEBOGEN 613 covers a convenient working range and remains compact and agile at the same time. With an uppercarriage width of only 2.55 m, the machine can also be transported easily and cost-effectively via flat-bed trailer.

The SENNEBOGEN 613 is powered by an economical 92 kW diesel engine with the Tier 4f emission standard. This new generation of engines not only meets the current requirements of the exhaust standards but also has an extremely economical consumption thanks to an optimized exhaust aftertreatment with DEF. In the future, the new SENNEBOGEN 613 will be available in two versions: with a mobile undercarriage and crawler traveling gear.

The SENNEBOGEN 613 E-Series – in summary

# Compact and powerful: 16 t lifting capacity, compact dimensions

# Full-Power Boom: Multi-part telescopic boom, always friction-locked, extremely robust design, continuously extendable and retractable via joystick-operated hydraulics (no 1-cylinder step procedure), length 18.8 m

# Easy transport – quickly operational: 2.55 m transport width, immediately ready for operation, folding 5 m tip

# Efficient: Powerful and efficient 92 kW diesel engine, Tier 4final exhaust aftertreatment

# Intuitive operation: SENCON control and diagnostics system for clearly laid-out and intuitive user control

- Comfortable operator area: New, ergonomic Multicab 2 operator cab